## Slide 1: Dynamic Programming for Power Systems
Aryan Ritwajeet Jha
Notes: Remember to hit the reset button to make sure all the page elements react properly.
There are 20 different layouts that you can choose from.

## Slide 2: Contents
Anamika Dubey and Surya Santoso (2015) Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation. It is a harder dynamic programming problem.
Problem Statements where Dynamic Programming is utilized.
  Recursive Fibonacci Sequence with Memoization.
  Shortest Path Problem with Memoization.

## Slide 3: Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation Anamika Dubey and Surya Santoso (2015)
EVs are plugged in during the night for charging.
Charging at multiple locations of the residential grid (a distribution network) at the same time causes voltage drops.
Such uncoordinated power consumption at the local scale can lead to grid problems.

## Slide 4: Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation Anamika Dubey and Surya Santoso (2015)
Context:
Charge M vehicles (loads) during night-time from M charging stations (nodes).
  Night-time = 6PM to 6AM.
Charge them fully before the next morning.
  They aren’t leaving before 6AM, so no hard constraints on the available charging timings themselves.

## Slide 5: Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation Anamika Dubey and Surya Santoso

## Slide 6: Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation Anamika Dubey and Surya Santoso
Objective:
minimize impact on residential grid voltage, for the whole night.
Design objective (constraint): Charge every EV fully by time T.

## Slide 7: Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation Anamika Dubey and Surya Santoso
Objective:
minimize impact on residential grid voltage, for the whole night.
Design objective (constraint): Charge every EV fully by time T.

## Slide 8: Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation Anamika Dubey and Surya Santoso
Design Formulation:
Battery-charger power levels P(t) variable only in discrete-steps. (zero, half-of-max-capacity, max-capacity)
Power-flow-analysis also done in discrete time-steps.
We’re solving a discretized Optimal Control Problem.
This is a ‘harder’ dynamic programming problem because of the boundary constraints.
Dynamic Programming Successive Approximation Method? Need to study it in detail.

## Slide 9
Dynamic Programming
Power System Optimization
Discrete Optimal Control Problem
Multi-time-period optimization work done here.

## Slide 10: Dynamic Programming
Bellman showed that a dynamic optimization problem in discrete time can be stated in a recursive, step-by-step form known as backward induction by writing down the relationship between the value function in one period and the value function in the next period. The relationship between these two value functions is called the "Bellman equation".

## Slide 11: Fibonacci Sequence using Dynamic Programming

## Slide 23: Shortest Path Problem using Dynamic Programming

## Slide 30: Do we even need a dynamic programming formulation in Power Systems?
Instead of using dynamic programming and optimization on
N state variables (including memory elements like Battery SOC)
C constraints
- All for T time steps
Why not just form:
N*T state variables (including Battery SOC)
C*T constraints plus T additional constraints to maintain continuity for those memory elements. (Let’s assume just one battery in our whole grid)
All into one big ‘steady-state-like’ Optimization problem and plug it into a solver?

## Slide 31: Do we even need a dynamic programming formulation in Power Systems?
Instead of using dynamic programming and optimization, why not just incorporate more state variables, more constraints (both by a factor of the number of time-steps: T) into one big ‘steady-state-like’ Optimization problem and plug it into a solver?
I do not have an answer for this now, I’d imagine that the time complexity will increase exponentially, but that’s just my speculation.

## Slide 32: References (not in order)
CTU Prague Optimal and Robust Control - L5.1 - Introduction to dynamic programming and its application to discrete-time optimal control
The Julia Programming Language - Dynamic Programming and Seam Carving | MIT Computational Thinking Spring 2021 | Lecture 6
Hu et al. (2016) - A Dynamic Programming based method for optimizing power system restoration with high wind power penetration
Guerrero, Heydt et al (2008) - Optimal Restoration of Distribution Systems Using Dynamic Programming
Anamika Dubey, Surya Santoso (2015) - Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigations
freeCodeCamp.org - Dynamic Programming - Learn to Solve Algorithmic Problems & Coding Challenges
Johan Driesen et al (KU Leuven, 2009) - The Impact of Charging Plug-In Hybrid Electric Vehicles on a Residential Distribution Grid