Weekly Summary
by Aryan Ritwajeet Jha
This week’s contents:
Problem: Solving for a power flow snapshot by decomposing a meshed grid into two radial grids and solving their individual power flows in parallel
Problem provided by Rabayet Sadnan

---
The Problem

---
End of This week’s contents.

---
Weekly Summary
by Aryan Ritwajeet Jha
This week’s contents:
Distributed Computing for Scalable Optimal Power Flow in Large Radial Electric Power Distribution Systems with Distributed Energy Resources
by Rabayet Sadnan and Anamika Dubey
PowerModelsDistributions.jl: An Open-Source Framework for Exploring Distribution Power Flow Formulations
By David M Fobes, Sander Claeys, Frederik Geth and Carleton Coffrin from LANL, KU Leuven

---
Weekly Summary
by Aryan Ritwajeet Jha
This week’s contents:
Network-Level Optimization for Unbalanced Power Distribution System: Approximation and Relaxation
by Rahul Ranjan Jha and Anamika Dubey
Distributed Optimizations Using Reduced Network Equivalents for Radial Power Distribution Systems
By Rabayet Sadnan and Anamika Dubey

---
Network-Level Optimization for Unbalanced Power Distribution System: Approximation and Relaxation
- Non-Linear Programming (NLP) to solve Distribution Level – Optimal Power Flow (D-OPF) poses convergence issues and not scalable for unbalanced power distribution systems (upds).
- Existing scalable solutions to D-OPF problem either use approximations that are not valid for upds or relaxation techniques not guaranteeing feasible power flow solution.

---
Network-Level Optimization for Unbalanced Power Distribution System: Approximation and Relaxation
- The authors scalable D-OPF algorithms have been proposed that simultaneously achieve optimal and feasible solutions by solving multiple iterations of approximate, or relaxed, D-OPF subproblems of low complexity.
- Algorithm 1 is based on successive linear approximation of Nonlinear Power Flow equations around the current operating point, where the D-OPF solution is obtained by solving multiple iterations of a linear programming problem.
- Algorithm 2 is based on the relaxation of the nonlinear power flow equations as conic constraints together with directional constraints, which achieves optimal and feasible solutions over multiple iterations of a second-order cone programming (SOCP) problem.

---
Network-Level Optimization for Unbalanced Power Distribution System: Approximation and Relaxation
- Applications of OPF algorithms:
  - Loss minimization
  - Volt-Var Optimization
  - Effective Management of DERs
- Need for Advanced Distributed Management Systems (ADMS)
  - Increasing penetration of DERs
  - Proliferation of Proactive loads
  - Interest in Demand Response Programmes

---
Distributed Optimizations Using Reduced Network Equivalents for Radial Power Distribution Systems
- Centralized Optimization Methods have limitations.
- Existing D-OPF algorithms not viable as they require a large number of macro-iterations (10^2 to 10^3 iterations of communication rounds) between computing agents to solve one instance of the optimization problem.
- So in the paper, the authors propose a new scalable D-Optimization method based on Equivalent Network Approximation (ENApp) to solve D-OPF for a balanced power distribution system (bpds).
- Specifically, the bpds’s radial topology is leveraged to reduced the decomposed systems into upstream and downstream network equivalents.
- Validated on IEEE 123 and IEEE 8500 systems and checked against the solution of a centralized optimal power flow (C-OPF) model.

---
Distributed Optimizations Using Reduced Network Equivalents for Radial Power Distribution Systems
- Typically C-OPF (which uses NLP) used to determine a pds’s operation == computational challenges and susceptibility to single point failure.
- In such a case D-O methods have these advantages:
  - Less computation load on a single machine
  - Less susceptibility to single-point failure due to multiple interacting agents
  - Relax the need between communication between a central controlling machine and connected controllable/non-controllable assets.